###### 07.04

###### Romberg Rule for Integration-More Examples

###### Chemical Engineering

# Example 1

In an attempt to understand the mechanism of the depolarization process in a fuel cell, an electro-kinetic model for mixed oxygen-methanol current on platinum was developed in the laboratory at FAMU.  A very simplified model of the reaction developed suggests a functional relation in an integral form.  To find the time required for 50 % of the oxygen to be consumed, the time,  is given by

Table 1  Values obtained using multiple-segment Trapezoidal rule.

|  | Value |
| --- | --- |
| 1 | 191190 |
| 2 | 190420 |
| 3 | 190260 |
| 4 | 190200 |

- Use Romberg’s rule to find the time required for 50 % of the oxygen to be consumed.  Use the 2-segment and 4-segment Trapezoidal rule results given in Table 1.

- Find the true error, , for part (a).

- Find the absolute relative true error, , for part (a).

# Solution

a)

Using Richardson’s extrapolation formula for Trapezoidal rule

and choosing n=2,

b) The exact value of the above integral is,

so the true error is

c) The absolute relative true error, , would then be

Table 2 shows the Richardson’s extrapolation results using 1, 2, 4, 8 segments.  Results are compared with those of Trapezoidal rule.

Table 2 Values obtained using Richardson’s extrapolation formula for Trapezoidal rule for

Trapezoidal Rule for Trapezoidal Rule % Richardson’s Extrapolation for Richardson’s Extrapolation % 1 2 4 8 191190 190420 190210 190150 0.55549 0.14838 0.037877 0.0095231 -- 190163 190127 190133 -- 0.014902 0.0043823 0.00087599

# Example 2

In an attempt to understand the mechanism of the depolarization process in a fuel cell, an electro-kinetic model for mixed oxygen-methanol current on platinum was developed in the laboratory at FAMU.  A very simplified model of the reaction developed suggests a functional relation in an integral form.  To find the time required for 50 % of the oxygen to be consumed, the time, is given by

Table 1 Values obtained using multiple-segment Trapezoidal rule. Value 1 191190 2 190420 3 190260 4 190200 5 190180 6 190170 7 190160 8 190150

Use Romberg’s rule to find the time required for 50 % of the oxygen to be consumed.  Use the 1, 2, 4, and 8-segment Trapezoidal rule results as given in the Table 1.

# Solution

From Table 1, the needed values from original Trapezoidal rule are

where the above four values correspond to using 1, 2, 4 and 8 segment Trapezoidal rule, respectively.  To get the first order extrapolation values,

Similarly

For the second order extrapolation values,

Similarly

For the third order extrapolation values,

Table 2 shows these increased correct values in a tree graph.

Table 2 Improved estimates of value of integral using Romberg integration.

# Text boxes

3rd Order

2nd Order

1st Order

190130

190130

190120

190130

190130

190160

190150

190200

190420

191190

8-segment

4-segment

2-segment

1-segment