###### Chapter 08.02

###### Euler’s Method for Ordinary Differential Equations-More Examples

###### Computer Engineering

# Example 1

A rectifier-based power supply requires a capacitor to temporarily store power when the rectified waveform from the AC source drops below the target voltage.  To properly size this capacitor a first-order ordinary differential equation must be solved.  For a particular power supply, with a capacitor of , the ordinary differential equation to be solved is

Using Euler’s method, find the voltage across the capacitor at .  Use step size .

# Solution

The Euler’s method reduces to

For , ,

is the approximate voltage at

For , ,

is the approximate voltage at

Figure 1 compares the exact solution of with the numerical solution from Euler’s method for the step size of .

Figure 1 Comparing exact and Euler’s method.

The problem was solved again using smaller step sizes.  The results are given below in

Table 1.

Table 1 Voltage at 0.00004 seconds as a function of step size, .

Step size, 0.00004 0.00002 0.00001 0.000005 0.0000025 106.64 53.307 26.640 15.996 15.993 90.667 37.333 10.666 0.021991 0.019125 567.59 233.71 66.771 0.13766 0.11972

Figure 2 shows how the voltage varies as a function of time for different step sizes.

Figure 2 Comparison of Euler’s method with exact solution for different step sizes.

While the values of the calculated voltage at as a function of step size are plotted in Figure 3.

Figure 3 Effect of step size in Euler’s method.

# Text boxes

h=240