###### Chapter 04.06

###### Gaussian Elimination – More Examples

###### Industrial Engineering

# Example 1

To find the number of toys a company should manufacture per day to optimally use their injection-molding machine and the assembly line, one needs to solve the following set of equations.  The unknowns are the number of toys for boys, , the number of toys for girls, , and the number of unisexual toys, .

Find the values of , , and  using naïve Gauss elimination.

# Solution

# Forward Elimination of Unknowns

Since there are three equations, there will be two steps of forward elimination of unknowns.

First step

Divide Row 1 by 0.3333 and then multiply it by 0.1667, that is, multiply Row 1 by .

Subtract the result from Row 2 to get

Divide Row 1 by 0.3333 and then multiply it by , that is, multiply Row 1 by .

Subtract the result from Row 3 to get

Second step

We now divide Row 2 by 0.58332 and then multiply it by , that is, multiply Row 2 by .

Subtract the result from Row 3 we get

# Back Substitution

From the third equation,

Substituting the value of  in the second equation,

Substituting the values of  in the first equation,

Hence the solution vector is

| SIMULTANEOUS LINEAR EQUATIONS |  |
| --- | --- |
| Topic | Gaussian Elimination – More Examples |
| Summary | Examples of Gaussian elimination |
| Major | Industrial Engineering |
| Authors | Autar Kaw |
| Date | August 6, 2009 |
| Web Site | http://numericalmethods.eng.usf.edu |